## Slide 1: Oxygenation Saturation Technology (OST®)
Presentation to the Lake Lawrence Management District
Paul Gantzer, Ph.D., P.E.

## Slide 2: (Gantzer) Background
Water Resources Management
Environmental Engineering
Navy Nuke
(ELT on board the
USS Carl Vinson)
Published over 20 peer reviewed articles 2007 – date on oxygenation/aeration and water quality management
Developed and patented OST®
United States,
Canada,
Australia, and
New Zealand

## Slide 3: Goal of this presentation
Thermal Stratification and anoxia
(Hypolimnetic) Oxygenation
Explain Oxygen Saturation Technology (OST®) what it is and how it works. (Benefit of oxygen management: Iron, phosphorus, ammonia and cyanobacteria)
Cover the basic characteristics of Cyanobacteria
Internal nutrient loading & phosphorus (sediment)
What oxygenation would look like and how it would work for Lake Lawrence.
Efficacy of internal nutrient loading management

## Slide 4: Why Oxygenate? Thermal Stratification / Anoxia
Algae
Detritus
Anoxia
Example schematic of water layers formed during stratification, showing epilimnion on top, metalimnion in the middle, and hypolimnion at the bottom.

## Slide 5: Getting Oxygen into the Water Hypolimnetic Oxygenation Specifically
Direct Injection Oxygenation
“Direct Injection” >50 ft
Saturation
“Side-stream Saturation” (SSS) < 50 ft

## Slide 6: What is OST®?
Oxygen Saturation Technology (OST®)
is an advanced aeration system
designed to overcome the challenges faced by traditional aeration methods
for all forms of oxygen management related to any aquatic environment, by
blanketing the sediments with oxygen.

## Slide 7: Oxygen Saturation Technology (OST®) Components and Relative Position
Onshore oxygen supply
Umbilical – O2 supply and pump power supply
OST® unit – pump & O2 contact chambers
Automation – DO Sensor
Suction & discharge headers
Suction
Discharge

## Slide 8: Oxygen Saturation Technology (OST®) US Patent US3643403A 2023-07-18
Key Design Characteristics
Uses oxygen gas (90% nominal purity produced from an on-site oxygen generator)
Buoyancy pipe (allows system to float for install/service and flooded to deploy/sink to bottom)
No bubbles / No mixing (No induced turbulence)
Preserves thermal structure (ice cover and/or summer stratification
Automated (DO feedback)
Achieve DO levels 5 X higher than traditional aeration
Modular and Scalable

## Slide 9: OST® - Oxygen Blanketing (Oxygen Placement focused at the Sediment)

## Slide 10: Graphical (data) Representation of Oxygen Blanketing

## Slide 11: Onshore Oxygen Supply (PSA)
Compressed Air Supply
Oxygen Generator
(Nitrogen Stripper)
Oxygen Receiving Tank

## Slide 12: Umbilical – O2 Supply & Pump Power Supply
Submersible Pump Cable
Oxygen Supply
Buoyancy
Anchor

## Slide 13: OST® Unit – Pump & O2 Contact Chambers
Conical Chamber
Bubble Capture Chamber
Water In
Water Out
Oxygen In
Pump
1
2
3
4
5
6

## Slide 14: Suction & Discharge Headers
100s of slotted openings covered with copper mesh.
Buoyancy Pipe
Discharge Header
Header Feet
Suction Header

## Slide 15: Automation – DO Sensor
DO Probe
Data Logger / Controller

## Slide 16: Strategies to Control Harmful Algal Blooms (HABs)

## Slide 17: What Are We Combating? A Crash Course in (Cyanobacteria) Biology.
Often referred to as ‘blue-green algae’
Evolved ~3.5 billion years ago, ubiquitous
Important physiological traits: dormant cells (akinetes), gas vesicles, secondary metabolites (toxins)
Important for nutrient cycling: nitrogen fixation and phosphorus storage

## Slide 18: Controlling Cyanobacteria(Theoretical)
Nutrient limitation:
  External nutrient control (runoff)
  Internal nutrient control (sediment phosphorous cycling)
    FePO4 Fe+3 + PO4-3
    Fe+3 + e- Fe+2
Disrupt cell structure / poison (algecide)
Disrupt sunlight exposure (mixing):
  Increase the depth of uniform temperature
  Decrease glycogen stores / increase pressure on gas vesicles
Proactive
Reactive

## Slide 19: Nutrients: Phosphate (PO4) Specifically. A Crash Course in RedOx Chemistry
Oxic
Anoxic
Nutrients

## Slide 20: Sediment P-speciation and P-Binding An overview of Internal P management

## Slide 21: Nitrogen and the Role it Plays with Phytoplankton A Crash Course in the Nitrogen Cycle (OST silver bullet)

## Slide 22: Nitrogen
Oxic
Anoxic
Cyanobacteria
Diatoms / Green Algae
Beutel (2001)
          Maintain DO ~ 10 mg/L over the sediments
Ammonia is the inorganic nitrogen source preferentially used by most cyanobacteria.

## Slide 23: Why Maintain DO >10 mg/L? Drive Oxic / Anoxic Boundary Deeper into Sediments
Bryan et al., (2010).

## Slide 24: Akinetes and the Sediment-Water Interface

## Slide 25: What would oxygenation for Lake Lawrence look like?

## Slide 26: Spanaway Design Example Layout

## Slide 27: Four (4) Large Systems in East Basin (~650 kg/d) Two (2) Small Systems in West Basin (~75 kg/d)

## Slide 28: Oxygen Distribution (Dispersion) *
1 mile
Carvins Cove Reservoir 2006

## Slide 29: Building Footprint and Examples
Custom
Built in Place
Pre-Cast
Stock
West
(200A/Single Phase)
East
(200A/Three Phase)

## Slide 30: How are piping and power cables secured?
All piping is HDPE.
All pipes are bundled 15-ft spacing.
All pipes are anchored with concrete anchors 15-ft spacing.

## Slide 31: What does operation look like? Daily Operation
Day to day operation is controlled by automation.
On-shore equipment is typical mechanical equipment and is recommended to have a daily inspection.
Additionally, on-shore equipment can also be connected to telemetry to provide messaging on conditions, i.e. low DO, low feed air pressure, etc.

## Slide 32: What does operation look like? Equipment Maintenance
Shore based equipment
In lake equipment
Buoyancy Pipe
Header Cleaning
Highly eutrophic: annually
Mesotrophic: Every 2 – 3 years
Performed by Lake Management Company
Preventative Maintenance
Per the PM schedule, typically bi-annually
Performed by Kaeser and/or AirSep Rep or equivalent

## Slide 33: OST® Recovery
10 Gallon Compressor

## Slide 34: OST® Deployment
2” Trash Pump

## Slide 35: This All Sounds Great in Theory. However, Will it Work?
Results

## Slide 36: Lake Lawrence P-Speciation: A Closer Look
High Organic P
Low Fe:P Ratio

## Slide 37: All “P” inactivation strategies only target the iron-bound (Fe-P) fraction!
More Iron = More Iron-Bound P

## Slide 38: Elk Lake (Direct Injection Oxygenation)
608 acre
58 ’ maximum depth
25 ’ average depth
Installed 2023

## Slide 39: Elk Lake Nitrogen and Phosphorus Results
Fe/Mn-bound phosphorus: 343 mgP/kg DW (41%),
organic-bound phosphorus: 488 mgP/kg DW (59%)
Ammonia is the inorganic nitrogen source preferentially used by most cyanobacteria.

## Slide 40: Foxwood Shores (Racine, WI)

## Slide 41: Sarah’s Pond Orleans, MA
Data courtesy of Ken Wagner of Water Resources Services, Inc.

## Slide 42: Clarity Recommendation for Lake Lawrence
Definitive evidence that:
iron + oxygen in shallow lakes can significantly reduce internal loading from organic-bound P.
+
Iron Amendment
OST®

## Slide 43: Did you learn the following:
The basics of Thermal Stratification and anoxia
How Oxygenation (OST®) manages oxygen
Better understating of P-inactivation and how it only applies to iron-bound phosphorus
The impacts of the organic-bound phosphorus
Why a dual approach of oxygenation and iron amendment are recommended (Fe deficiency & high organic-bound P)
Understanding that a Clarity approach is focused on solving the problem, not just adding oxygen.

## Slide 44: Cost: Capital, Operational, and Maintenance
OST (725 kg-O2/day to the hypolimnion) Estimated Cost: $2,000,000*
*Does not include: Site work, building, electrical, ventilation, permitting, taxes
Iron amendment (ZVI) Cost: TBD

## Slide 45: How Long Will it Last? The equipment or the treatment?
Oxygenation is not a service like other approaches. The application of oxygen is not a one and done, it is an ongoing strategy that will be required for the life of the lake.
This question is being addressed from a “mechanical” lifespan not a “how long will a chemical dose last.” Therefore:
All HDPE components are rated for 50+ years.
Oxygen Generator: No documented failure if PM schedule is followed.
Compressor: Depends on operating conditions and adherence to PM schedule. Motor replacement estimated from 10 – 20 years.
Submersible pump: No documented failure from other projects that were installed 10+ years ago. However, it would be recommended to budget for 10 yr replacement

## Slide 46: Thank You

## Slide 47: Why Not Just Add More Iron? A case study by University of Minnesota.
Before